May O6 Experiment Plan

| Parameter | Value |
| --- | --- |
| Frequency | 150 Mhz |
| Band width | 20 MHz |
| Range window | Start 4 us to 44 us with pulse 1 (lo-gain) Then 15 us to 55 us pulse 2 (hi-gain) |
| Pulse width | 3 us |
| PRF | 10 KHz (5 Khz for each pulse) |
| Baseline offset | Return flight 25 m south of outbound flight |
| Calibration | Rough ocean observations at these specs |
| Aircraft elevation above ellipsoid (geoid) | 10,000 -12000 ft (install additional external attunuators into the receiver |
| Options |  |
| High elevation flight in south Greenland on any flights of opportunity | 10,000 ft |
| At end of project, switch to 2 transmit element and 6 receive elements | r r r b b t b b b r r r which means about a 7 m baseline (r=receiver, b= blank, t= transmit) r r r b t t b r r r (ping pong) |
| Early evaluation of Greenland data | VECO assisted DVD or electronic file transfer to KU after first GISMO flight: Process to depth sounder mode; Process to SAR image |